## Slide 1: Dependence of apparent viscosity of blood on strain rate
Decrease of apparent viscosity of blood with increasing shear strain rate occurs due to creation of aggregates of blood cells under low shear rates and,vice versa, their disturbance under higher shear rates.
Dispersion of the apparent viscosity is mostly due to changes in temperature and hematocrit (volume fraction of erythrocytes).
At 37°C the viscosity is
- for blood 3,0-3,6.10-3 Pa.s (under strain rates >100s-1),
for blood plasma 2,0.10-3 Pa.s,
for water 1,0.10-3 Pa.s.

## Slide 2: Simplest models of rheologic properties of blood
Here k is the time relaxation constant, η∞ is the apparent viscosity for high strain rates (>100 s-1) while η0 is the apparent viscosity limit for very small strain rates.
The model was originally derived for , for which n=2/3 was recommended.
*) Cross, M.M. (1965) Rheology of Non-Newtonian Fluids—A New Flow Equation for Pseudoplastic Systems. Journal of Colloid Science, 20, 417-437. http://dx.doi.org/10.1016/0095-8522(65)90022-X.
Power law model – for a limited range of strain rates (cca 1-10 s-1)
Cross*) model – for a wider range of strain rates (cca 1-100 s-1)
Notes: Publikace Mimouni, ze které je power law model, je nevěrohodná a neuvádí hodnoty konstant, chtělo by to dohledat originální zdroje. Vztah opravit podle originální publikace (je v Maple). Mám z publikace. Mimouni Z. :The Rheological Behavior of Human Blood – Comparison of Two Models. Open Journal of Biophysics, nemá IF a je nevěrohodná.

## Slide 3: Carreau model of rheologic properties of blood
Available approximations:
η0=56 mPas; η∞=3,45 mPas; k=3,31 s; q=0,375
Approximation made by Gambaruto*)
η0=45,6 mPas; η∞=3,2 mPas; k=10,03 s; q=0,344*)
Here k is the time relaxation constant, η∞ is the apparent viscosity for high strain rates (>100 s-1) while η0 is the apparent viscosity limit for nearly zero strain rates.
*) Gambaruto, A.M., Janela, J., Moura, A. and Sequeira, A. (2011): Sensitivity of Hemodynamics in a Cerebral Aneurysm Patient Specific to Vascular Geometry and Blood Rheology. Mathematical Biosciences and Engineering, 8, 409-423.
http://dx.doi.org/10.3934/mbe.2011.8.409Carreau & Gambaruto:

## Slide 4: Casson model of rheologic properties of blood
The formula is based on the experimentally obtained linear dependence between square roots from these quantities, thus it holds:
The common form of Casson model specifies the dependence between shear stress and shear strain rate as follows:
where are material parameters.

## Slide 5: Graph of rheologic properties of blood
Chart: Casson model of blood viscosity
| 0.70710678118654757 | 1 | 1.4142135623730951 | 3.1622776601683795 | 7.0710678118654755 | 10 | 31.622776601683793
Závislost odhadnutá podle grafu viskozity | 0.1 | 0.1 | 0.10954 | 0.2 | 0.42426 | 0.59161 | 1.8708

## Slide 6: Dependence of apparent blood viscosity on shear strain rate
Chart: Casson model of blood viscosity
| 0.25 | 1 | 4 | 100 | 2500
1. aproximace (na menším rozsahu) | 0.009604 | 0.006084 | 0.004624 | 0.0036 | 0.0034106
2.aproximace (na větším rozsahu) | 0.013759 | 0.0076213 | 0.0040069 | 0.0034222 | 0.0033524 | 0.0032902
Automatická aproximace | 0.014137 | 0.0078146 | 0.0053509 | 0.0037149 | 0.0034234 | 0.0033878 | 0.0033559

## Slide 7: Graph of rheologic properties of blood from the basic approximation of Casson model
Chart: Casson model of blood viscosity
| 0 | 20 | 40 | 60 | 80 | 100 | 120 | 140
 | 0.0305 | 0.18795 | 0.29245 | 0.38823 | 0.4795 | 0.56789 | 0.65423 | 0.73902
It is combination of bingham plastic and pseudoplastic behaviour.

## Slide 8: Quemada model considering also hematocrit
Its formulation is as follows:
where
or alternatively
Critical time τ characterizes the evolution of the structure (as for instance a time for particle aggregation or, more generally, a mean relaxation time).
Alternatively, the critical shear rate appears as related to the critical shear stress under which the structure is broken.
Model parameters:
η∞=1,2 mPas represents plasma viscosity; k∞=2,07; k0=4,33; =1,88 s-1;
hematocrit H=45%.
*) Quemada D.: A Rheological Model for Studying the Hematocrit Dependence of Red Cell-Red Cell and Red Cell-Protein Interactions in Blood. Biorheology (1981) 18(3-6):501-16.
Notes: Vztah i obrázek mám z publikace. Mimouni Z. :The Rheological Behavior of Human Blood – Comparison of Two Models. Open Journal of Biophysics, nemá IF a je nevěrohodná. Model Quemada musím dohledat v originále.